## Slide 1: Multiprocessor caching and false sharing

## Slide 2: Recall: Caching
Cache(s) sit between processor and memory
  Handle memory accesses w/o going all the way to memory
  Exploit temporal locality and spatial locality
Notes: Brief review of caching, with brief animation showing how it works

## Slide 3: Recall: Caching
Cache(s) sit between processor and memory
  Handle memory accesses w/o going all the way to memory
  Exploit temporal locality and spatial locality
request
Notes: On a memory request, if the data isn’t in the cache, the request is passed all the way to memory

## Slide 4: Recall: Caching
Cache(s) sit between processor and memory
  Handle memory accesses w/o going all the way to memory
  Exploit temporal locality and spatial locality
request
response
Notes: The response traces this path back to the processor, but also stores the desired data into the cache

## Slide 5: Recall: Caching
Cache(s) sit between processor and memory
  Handle memory accesses w/o going all the way to memory
  Exploit temporal locality and spatial locality
request
response
Notes: Subsequent requests don’t have to go to memory since the cache can satisfy the request

## Slide 6: Recall: Caching
Cache(s) sit between processor and memory
  Handle memory accesses w/o going all the way to memory
  Exploit temporal locality and spatial locality
Store lines that with recently accessed memory locations and other locations nearby
request
response
Notes: Key point of this slide is that a cache line also stores data near the accessed memory address. This is what makes caches useful for spatial locality

## Slide 7: Caching for multiple processing elements (PEs)
Notes: With multiple processors (or cores), caches can be shared or private. (In practice, a system can have multiple layers of caching so it may have both…)
We’re going to focus on private ones

## Slide 8: Cache coherence
request
Potential issue when cache line is in one cache and other PE requests it
Notes: Private caches raise new challenge: If a cache line is stored on one of the private caches and the other processing element requests it, that PE’s cache won’t have the newest value and neither will the memory

## Slide 9: Cache coherence
request
Potential issue when cache line is in one cache and other PE requests it
Cache of requesting PE needs way to steal that line

## Slide 10: Cache coherence
request
Potential issue when cache line is in one cache and other PE requests it
Cache of requesting PE needs way to steal that line
Slower than normal cache hit because of need to steal
Notes: This incurs a cost in complexity to know when a line needs to be stolen and in time for each steal operation

## Slide 11: Cache coherence
request
Potential issue when cache line is in one cache and other PE requests it
Cache of requesting PE needs way to steal that line
Slower than normal cache hit because of need to steal
False sharing: When a memory access causes a cache line to be stolen even though no data is actually being shared
Notes: Finally can introduce idea of false sharing. Follow up by going through the code (or having the students do so)
Key point is that because cache lines contain more than one data item, the two PEs might not share data, but might share cache lines. This can create significant unnecessary costs if they repeatedly steal the line from each other